## Slide 1
Airspace Integration of Launch and Reentry Operations

## Slide 2
Airspace Integration of Launch and Reentry Operations
FAA Air Traffic Organization
Overview
Risk Assessment and Aircraft Hazard Area Development
Mission Planning
Traffic Flow Management
Real-Time Mission Support
Post Operations Analysis

## Slide 3
  Space Operations
  Safe Integration of Space Launches
  Space Operations Overview

## Slide 4
  Office of Commercial Space Transportation (AST)
  License/Permit, Regulate and Inspect United States commercial space industry
  Air Traffic Organization
  (ATO)
  Integrate launch and reentry operations, commercial and non-commercial into the National Airspace System (NAS)
  ATO System Operations (AJR)
  ATO Space Operations (AJR-1800)
  Federal Aviation Administration

## Slide 5
FAA Air Traffic Organization Space Operations
Our Mission: Ensure space launch and reentry operations are safely and efficiently integrated into the National Airspace System (NAS)

## Slide 6
Notes: Present day Spaceports with additional proposals.
Note the Spaceports that are within SUA
--Space Port America
--Mohave

## Slide 7
Common Themes
  Shared situational awareness among operator, range/spaceport and Air Traffic Control (ATC)
  Collaboration between operator, range/spaceport, ATC, and international stakeholders

## Slide 8
Airspace Integration
Risk Assessment and Aircraft Hazard Area Definition

## Slide 9
Risk Assessment
Risk assessment performed by operator, range/spaceport and/or regulator
  Air, Sea, and Land risks are assessed and have different thresholds
  Aircraft Hazard Areas (AHAs) defined by regulation and policy as 1x10-6 for casualty-producing collisions
  FAA ATO adds additional non-regulatory requirements associated with space operations “Acceptable Level of Risk (ALR)”
    ALR was added to bridge the gap between regulatory requirements 1x10-6 and ATO target level of safety of 1x10-9
  Risk Assessment also includes debris fall times associated with nominal and malfunction

## Slide 10
Risk Assessment
Risk Analysis: Risk contours are developed representing the risk to aircraft operations in the vicinity of launch or reentry operations
Green Contour = 1x10-8 Risk
Yellow Contour = 1x10-7 Risk
Light Red Contour = 1x10-6 Risk
Red Contour = 1x10-5 Risk

## Slide 11
Risk Assessment
Aircraft Hazard Areas (AHAs): AHAs are developed to contain the risk contours that represent 1x10-6 risk to aircraft operations
Red Line/Box = AHA
Green Contour = 1x10-8 Risk
Yellow Contour = 1x10-7 Risk
Light Red Contour = 1x10-6 Risk
Red Contour = 1x10-5 Risk

## Slide 12
Risk Assessment
AHAs: AHA are implemented for different stages of a launch operation
  Vehicle launch and ascent area
  Jettison item area
  Stage reentry area
Jettison Item AHA
Ascent AHA
Launch AHAs
Reentry AHA

## Slide 13
Risk Assessment
Acceptable Level Of Risk (ALR):
ALR was added to bridge the gap between regulatory requirements and ATO target level of safety of 1x10-9
1x10-7 Hazard Areas are Debris Response Areas (DRAs), which are used as a contingency in the event of a launch malfunction. DRA activation times are calculated using the risk analysis malfunction times
1x10-8 Hazard Areas are used for data collection associated with annual collective risk thresholds
Green Contour = 1x10-8 Risk
Yellow Contour = 1x10-7 Risk
Light Red Contour = 1x10-6 Risk
Red Contour = 1x10-5 Risk

## Slide 14
Risk Assessment
New Procedures – Debris Response Areas (DRAs):
Real-time ATO response to a debris-generating event:
  Appropriate DRA will be activated based on the time of the vehicle malfunction
  DRA will be evacuated and remain sterile until all debris has fallen to earth
  DRA durations are pre-calculated and known prior to the launch
  Applied in radar-controlled airspace only
DRA #1
DRA #2
DRA #3

## Slide 15
Risk Assessment
Risk Analysis:
AHA Activation Times
  Nominal operations
  Malfunction operations
  (debris fall time)
Nominal
Malfunction

## Slide 16
Airspace Integration | Module
Mission Planning

## Slide 17
Mission Planning
Summary 5-Step Process: (typical operation)
  Operator notification of intent to launch – 10 days prior
  Mission Engineers create images and load SDI – 10 to 8 days prior
  Evaluation/Analysis of mission specifics – 7 to 5 days
  Stakeholder outreach – 4 to 1 days (i.e. Airspace Management Plan)
  Hotline Activation and Launch – day of operation
Planning and Coordination

## Slide 18
Mission Planning
Notification:
  Operator intent
    Dates
      Primary
      Back up
    Launch window
    Intended launch time(s)
  Risk analysis products
    AHA definition
    Nominal closure times
    Malfunction closure times
    Reentry times
Operator Intent to Launch
Range Safety Analysis

## Slide 19
Mission Planning
AHA Definition:
  Lateral AHA dimensions
  Launch window
  Malfunction times
Launch window = 0205-0432 UTC
Malfunction times: AHA A = 25 mins
AHA B = 47 mins
Activation Time = Launch Window + Malfunction Time
AHA A activation = 0205-0457 UTC
AHA B activation = 0205-0519 UTC
Jettison Item AHA
Ascent AHA
Launch AHAs
Reentry AHA

## Slide 20
Mission Planning
Evaluation: Assessment of impacts on airspace system is performed using
  AHA definition
  Historical aviation traffic data

## Slide 21
Mission Planning
International Coordination
  Process typically initiated 10 days before launch
  ATO Space Operations initiates coordination with International Air Navigations Service Providers (ANSPs) and U.S. NOTAM Office
  Danger Areas published for hazard
  Aeronautical Messaging Handling Service (AMHS) preferred method of coordination

## Slide 22
Mission Planning
Airspace Management Plan:
  Mission Overview
  Mission Schedule
  Traffic Management Initiatives
  Distribution:
    LRO
    Range
    ATC Facilities
    Aviation Community
    Other Stakeholders

## Slide 23
Airspace Integration | Module
Traffic Flow Management

## Slide 24
Traffic Flow Management:
Traffic management predominately consists of route management
Use of time-based procedures minimizes the total impact of operations
Real-time situational awareness is key to tactical management of airspace and aircraft during operation
Collaborative discussions with the space industry have been critical to understanding operations and the development of dynamic airspace management procedures
Early communication of traffic management plan to the aviation industry is important (i.e. planning telcon)

## Slide 25
Traffic Flow Management:
Use of time-based procedures minimizes the total impact of operations
Importance of hotline in tactical management of aircraft during operation
Collaborative discussions with industry have been critical to understanding operations and the development of dynamic airspace management procedures

## Slide 26
Airspace Integration | Module
Real-Time
Mission Support

## Slide 27
Real-Time Mission Support
Mission: Ensure space launch and reentry operations are safely and efficiently integrated into the National Airspace System (NAS)
  Conducted from the Challenger Room at the FAA Air Traffic Control System Command Center in Warrenton, Virginia.
  Key Tools:
    Space Data Integrator (SDI)
    Traffic Flow Management System
    Hotline

## Slide 28
Real-Time Mission Support
Hotline Actions:
  The hotline is key to real-time shared situational awareness
  Operator call out of key mission events
  Airspace is tactically managed and deactivated (TBLP/DLRW)
  Traffic Management initiatives are canceled
  In the event of a launch malfunction, Debris Response Areas (DRAs) are activated and canceled
ATC Facilities
Federal Range
DoD Commands
Operator
NORAD
Commercial Range

## Slide 31
Airspace Integration | Module
Post Operations Analysis

## Slide 32
Post Operations Analysis
Lessons Learned
Data Analysis
Best Practices